## Slide 1: Edge Intelligence I: Foundations & The Substrate
Topic: What is Edge Intelligence | Hardware | Software
Chapter 4

## Slide 2: Outline
What is Edge Intelligence
AI meets the edge
Training vs inference
Why intelligence moves out
Computing Models
CPU & GPU baseline
ASIC, FPGA, Jetson
Performance metrics
Software
Frameworks & runtimes
Lite & mobile engines
Development stack
Summary & Practice
Summary
Practice

## Slide 3: Edge Intelligence: Motivation
Pushed by edge computing
IoT data, edge devices, storage, wireless links and on-device security make it feasible to run AI where data is born.
Pulled by AI applications
Connected health, vehicles, smart manufacturing, smart homes and video analytics all demand real-time, on-site inference.
The edge handles video, speech, time-series and sensor data with no round-trip to the cloud.
Motivation of edge intelligence

## Slide 4: Edge Intelligence: Definition
International Electrotechnical Commission. Edge Intelligence. https://www.iec.ch/basecamp/e dge-intelligence. Accessed: 2024-05-27. 2024
Edge intelligence is the capability of edge devices to execute artificial-intelligence algorithms locally, acquiring, storing and processing data with ML at the network edge.
Because hardware differs, every edge has a different EI capability — captured by the ALEM tuple:
Accuracy
Quality of the model’s output (e.g. mAP, BLEU). Compression trades some of it away.
Latency
Inference time per task — the measure of edge performance under load.
Energy
Extra power drawn while running inference on the device.
Memory
Footprint of the model in memory during execution.

## Slide 5: Edge Intelligence: Collaboration
Two ways Edges cooperate
Cloud – Edge
Train in the cloud, download to the edge for inference. Edges may retrain locally via transfer learning and push updates back to a global model — e.g. DDNN spans cloud and edge.
Edge – Edge
Edges split one heavy job by compute power or divide a task by context. A phone predicts you’re nearly home and cues the thermostat: hard alone, easy in concert.
Edge Intelligence

## Slide 6: Edge Intelligence: Data Flows
Three ways to use edge data
Dataflow of edge intelligence
Cloud training
Upload to cloud, train on multi-source data, infer, return result. Traditional machine intelligence.
Edge inference
Run the cloud-trained model on-device against local data. The current EI dataflow.
Edge local training
Retrain on-device with transfer learning to build a personalized model. The future of EI.

## Slide 7: Edge Intelligence: Case For EI
Why intelligence moves to the edge
Latency
Decisions happen next to the data. No cloud round-trip for face ID, speech, or driving.
Bandwidth
Raw video and sensor streams stay local; only results or model updates travel.
Privacy
Sensitive data is processed on-device, lowering the risk of interception or leakage.
Reliability
Works offline and near the source. Resilient when the network is weak or down.

## Slide 8: Hardware: Case For EI
Unlike cloud data centers, edge devices run under tight compute and power budgets. Five families cover the field.
CPU
Flexible, everywhere
General control & light inference
GPU
Massively parallel
Deep learning, autonomous systems
FPGA
Reconfigurable
Custom, adaptive AI workloads
ASIC
Fixed-function
Peak efficiency: TPU, VPU, NPU
Neuromorphic
Brain-inspired
Spiking, sensory, cognitive

## Slide 9: Hardware: CPU & GPU
CPU
Serial, general-purpose control logic
Runs the OS, orchestration, glue code
Handles light or infrequent inference
Ubiquitous — every edge device has one
Poor throughput on dense tensor math
GPU
Thousands of cores for parallel math
The workhorse for deep-learning training
Strong on batched, high-throughput inference
Jetson brings GPU compute to the edge
Costs the most power of the edge options

## Slide 10: Hardware: ASIC
An ASIC is hard-wired for a specific task, sacrificing flexibility for the best accuracy, latency and energy in its niche.
TPU
Google Edge TPU
Tensor Processing Unit tuned for TensorFlow inference — image classification & object detection at very low power.
VPU
Intel Movidius Myriad X
16 SHAVE cores + a neural engine, >1 TOPS. Vision-centric: facial recognition, visual SLAM, low-power detection.
Neuromorphic
IBM TrueNorth · Intel Loihi
Brain-inspired, highly parallel & efficient — real-time pattern recognition, robotics, cognitive computing.

## Slide 11: Hardware: FPGA & GPU
FPGA
Xilinx (Alveo, MPSoC) & Intel (Agilex, Stratix 10)
Arm cores + programmable logic → real-time, low-power
ESE ran sparse LSTM faster & greener than CPU/GPU
Studies find FPGA well-suited to EI workloads
Jetson
Jetson Nano — 472 GFLOPs at just 5–10 W
AGX Xavier — 512-core Volta GPU + 8-core CPU
CUDA + TensorRT accelerate robotics & AV workloads
Jetson Orin (2022) scales to complex edge AI

## Slide 12: Hardware: Comparison of Hardware Types for Edge AI Applications
Type
Sub-type
Examples
AI performance
Power eff.
Latency
Key applications
ASIC
TPU
Google TPU,
Google Edge TPU
Excellent for AI inference, optimized for TensorFlow
Very low
Real-time AI inference, image classification, object detection
VPU
Intel Movidius
Myriad X
High for vision-centric AI tasks
Low
Facial recognition, visual SLAM, low-power object detection
Neuromorphic chip
IBM TrueNorth,
Intel Loihi
Efficient for brain-inspired AI models
Very low
Cognitive computing, robotics, sensory processing
FPGA
—
Xilinx UltraScale+,
Intel Stratix
High, customizable for specific AI workloads
Low to moderate
Custom AI models, adaptive AI tasks
GPU
—
Jetson Nano,
AGX Xavier
High, particularly in parallel processing tasks
Medium
Deep learning, autonomous systems, AI research
Power efficiency
= high
= moderate
= very high
= extremely high

## Slide 13: Software: Frameworks
Cloud-first
Built to train at scale
TensorFlow, Caffe, MXNet, PyTorch
Large datasets, learn millions of weights
Run on GPU / CPU / FPGA / TPU clusters
Resource-hungry — a poor fit for edges
Edge-optimized
Built to infer on-device
Same inference, far fewer resources
Small-scale, real-time input data
Installed on phones, Pi, laptops, servers
Optimized kernels & quantization
TensorFlow Authors. TensorFlow Lite. https://www.tensorflow.org/lite. Accessed: 2024-05-21. 2024.
Tianqi Chen et al. “MxNet: A flexible and efficient machine learning library for heterogeneous distributed systems”. In: arXiv preprint arXiv:1512.01274 (2015).
Cloud Frameworks Don’t Fit the Edge

## Slide 14: Software: Lite/Mobile Runtime
TensorFlow Lite
Google’s mobile/edge runtime — fused, quantized kernels cut latency.
ONNX Runtime
Cross-platform engine (Meta + Microsoft); runs on Jetson, FPGA, NPU, AGX.
Core ML
Apple’s on-device package — minimal memory & power
QNNPACK / XNNPACK
Meta & Google low-level kernels for quantized & float inference.
OpenVINO
Intel toolkit — converts TF/PyTorch models, deploys across Intel HW.
Vitis AI · FINN
Xilinx FPGA stacks — optimize, compile & quantize for the fabric.
Azure IoT Edge
Microsoft — deploy & manage cloud-native AI workloads on devices.
SageMaker Neo · TensorRT
AWS & NVIDIA — compile once, accelerate inference on target HW.
Amazon Web Services, Inc. Amazon SageMaker Neo: Train Once, Run Anywhere. https://aws.amazon.com/sagemaker/neo/. Accessed: 2024-08-21. 2024.
AMD Xilinx. Vitis AI. https://www.xilinx.com/products/design-tools/vitis/vitis-ai.html. 2024.
Apple Inc. Core ML Documentation. https://developer.apple.com/documentation/coreml. Accessed: 2024-05-20. 2024.
Google. XNNPACK. https://github.com/google/XNNPACK. GitHub repository. 2024.
Intel. OpenVINO Toolkit Overview. https://www.intel.com/content/www/us/en/developer/tools/openvino-toolkit/overview.html. Accessed: 2024-07-10. 2024.
Dukhan Marat, W. Yiming, and L. Hao. QNNPACK: Open source library for optimized mobile deep learning. 2018.
Microsoft. Azure IoT Edge. https://azure.microsoft.com/en-us/products/iot-edge. Accessed: 2024-07-10. 2024.
NVIDIA Corporation. TensorRT. https://developer.nvidia.com/tensorrt. Accessed: 2024-05-20. 2024.
ONNX Runtime Developers. ONNX Runtime. https://onnxruntime.ai/. 2021.
Yaman Umuroglu et al. "FINN: A framework for fast, scalable binarized neural network inference". In: Proceedings of the 2017 ACM/SIGDA International Symposium on Field-Programmable Gate Arrays. 2017, pp. 65–74.

## Slide 15: Software: Deployment
Runtimes & Containers: The Stack
Running Environments
TinyOS — event-driven OS for sensor networks
ROS / ROS 2 — robotics; DDS messaging, no master
AWS IoT Greengrass — deploy AI to fleets of devices
OpenVDAP · EdgeOS_H — vehicle & smart-home stacks
SageMaker Edge — compile & manage models on devices
PYNQ — Python on Xilinx Zynq FPGA + Arm SoCs
Containers
Bundle code, runtime, libraries & deps into one portable unit.
Share the OS kernel — small, resource-efficient, easy to migrate.
Engines: Docker, RKT, LXD, Kubernetes.
Container architecture over a shared kernel

## Slide 16: Summary
Edge intelligence is the capability of edges to run AI algorithms locally, measured by ALEM (Accuracy, Latency, Energy, Memory).
Cloud-edge and edge-edge collaboration split training and inference across the continuum.
CPU, GPU, FPGA, ASIC (TPU/VPU) and neuromorphic chips trade flexibility for efficiency.
Lite runtimes, edge OSs and containers turn silicon into portable, efficient intelligence.

## Slide 17: Practice
1
How does edge hardware differ from traditional data-center hardware?
2
Discuss the advantages and challenges of implementing machine learning at the edge?
3
What are the key considerations in choosing an edge application development framework?
5
6

## Slide 18: References
International Electrotechnical Commission. Edge Intelligence. https://www.iec.ch/basecamp/e dge-intelligence. Accessed: 2024-05-27. 2024.
TensorFlow Authors. TensorFlow Lite. https://www.tensorflow.org/lite. Accessed: 2024-05-21. 2024.
Tianqi Chen et al. “MxNet: A flexible and efficient machine learning library for heterogeneous distributed systems”. In: arXiv preprint arXiv:1512.01274 (2015).
Amazon Web Services, Inc. Amazon SageMaker Neo: Train Once, Run Anywhere. https://aws.amazon.com/sagemaker/neo/. Accessed: 2024-08-21. 2024.
AMD Xilinx. Vitis AI. https://www.xilinx.com/products/design-tools/vitis/vitis-ai.html. 2024.
Apple Inc. Core ML Documentation. https://developer.apple.com/documentation/coreml. Accessed: 2024-05-20. 2024.
Google. XNNPACK. https://github.com/google/XNNPACK. GitHub repository. 2024. Intel.
OpenVINO Toolkit Overview. https://www.intel.com/content/www/us/en/developer/tools/openvino-toolkit/overview.html. Accessed: 2024-07-10. 2024.
Dukhan Marat, W. Yiming, and L. Hao. QNNPACK: Open source library for optimized mobile deep learning. 2018.
Microsoft. Azure IoT Edge. https://azure.microsoft.com/en-us/products/iot-edge. Accessed: 2024-07-10. 2024.
NVIDIA Corporation. TensorRT. https://developer.nvidia.com/tensorrt. Accessed: 2024-05-20. 2024.
ONNX Runtime Developers. ONNX Runtime. https://onnxruntime.ai/. 2021.
Yaman Umuroglu et al. "FINN: A framework for fast, scalable binarized neural network inference". In: Proceedings of the 2017 ACM/SIGDA International Symposium on Field-Programmable Gate Arrays. 2017, pp. 65–74.