## Slide 1: Edge Intelligence III: Codesign & Edge Systems
Topic: Low-rank approximation | HW-SW codesign | Lightweight Models | Training & Inference
Chapter 4

## Slide 2: Outline
Low-Rank Approximation
Factor big weight matrices
SVD & rank intuition
Fewer params, less compute
HW-SW Codesign
Co-develop model + chip
CODEBench, TransPIM
FPGA & multimodal codesign
Lightweight Models
MobileNet, SqueezeNet
Tiny models: Bonsai, FastGRNN
MobileViT hybrids
Summary & Practice
Acceleration Techniques
Model simplification
Auto-ViT-Acc
ViA FPGA accelerator
Training & Inference
Edge training architectures
CLONE collaborative learning
TensorRT & collaborative infer

## Slide 3: Low-Rank Approximation
What is rank?
Denton et al. SVD on FC layers → 3× conv speedup, <1% precision loss.
Denil et al. Low-rank cuts the number of dynamic parameters.
Sainath et al. Low-rank factorization on the final DNN layer for acoustic models.
The number of linearly independent rows/columns — a measure of how much unique information a matrix holds. Correlated rows → low rank → compressible.
Original weight W
m x n full rank | dense
m . n parameters
U
m x k
V
k x n
Only k (m + n) parameters
≈
Low-rank factors U x V
Rank k << min(m, n)
Decompose one big multiplication into two small ones
Correlated rows mean W is effectively low-rank- SVD or factorization recovers it, cutting compute.
Emily L Denton et al. "Exploiting linear structure within convolutional networks for efficient evaluation". In: Advances in Neural Information Processing Systems 27 (2014).
Misha Denil et al. "Predicting parameters in deep learning". In: Advances in Neural Information Processing Systems 26 (2013).
Tara N Sainath et al. "Low-rank matrix factorization for deep neural network training with high-dimensional output targets". In: 2013 IEEE International Conference on Acoustics, Speech and Signal Processing. IEEE. 2013, pp. 6655–6659.
Factor the Weight Matrix

## Slide 4: Low-Rank Approximation: Singular Value Decomposition (SVD)
SVD provides fewer parameters with less compute
Original weight W
m x n full rank | dense
m . n parameters
Ur
Vᵣᵀ
Truncate to rank r
For deployment, absorb Σᵣ into either factor: A = UᵣΣᵣ, B = Vᵣᵀ
m × r
r × r
r × n
Σᵣ
One large multiply becomes two smaller multiplies
SVD preserves the dominant structure of W while discarding low-information directions.
Less memory • Fewer MACs • Faster inference
Efficiency Gain
Parameters
Before mn After r(m +n)
Example
W = 1024 × 1024
1,048,576
r = 128
262,144
≈ 75% fewer parameters
Compute
O(mn) → O[r(m+n)]
Truncated Singular Value Decomposition

## Slide 5: Hardware-Software (HW-SW) Codesign
Model and hardware should be designed together for edge
The idea.
Software and hardware are developed simultaneously to maximize an edge device’s performance, efficiency and scalability.
Software part
Compression, kernel & memory optimization, parallelization, resource management, libraries.
Hardware part
Low-power cores, accelerators & hardware resources tuned to the workload.
Overview of hw-sw codesign

## Slide 6: HW-SW Codesign: Frameworks
CODEBench pipeline that includes CNNBench, AccelBench, and a novel co-design method, BOSHCODE: (a) The CNN and accelerator design spaces are sampled for novel CNN-accelerator pairs that are simulated using the CNNBench and AccelBench frameworks. (b) BOSHCODE learns a surrogate function from these design spaces to predict the performance of each CNN-accelerator pair, implementing GOBI to predict the next pair to be simulated in the active learning framework.
CODEBench
Pairs CNNBench (Bayesian architecture search) with AccelBench (cycle-accurate accelerator sim). Beats SOTA on ImageNet & Cifar for accuracy, latency and energy.
CODEBench
Shikhar Tuli et al. “CODEBench: A neural architecture and hardware accelerator co-design framework”. In: ACM Transactions on Embedded Computing Systems 22. 3 (2023), pp. 1–30.

## Slide 7: HW-SW Codesign: Frameworks
TransPIM
software–hardware codesign for transformers via processing-in-memory. Token-based dataflow + light HBM tweaks give 2.0× the throughput of ASIC accelerators.
TransPIM
Minxuan Zhou et al. “TransPIM: A memory-based acceleration via software-hardware codesign for transformer”. In: 2022 IEEE International Symposium on High-PerformanceComputer Architecture (HPCA). IEEE. 2022, pp. 1071–1085.
Token-based data sharding scheme and the dataflow of Transformer encoder in TransPIM.

## Slide 8: HW-SW Codesign: Frameworks
Additional
Cong Hao and Deming Chen. “Software/hardware co-design for multi-modal multi-task learning in autonomous systems”. In: 2021 IEEE 3rd International Conference on Artificial Intelligence Circuits and Systems (AICAS). IEEE. 2021, pp. 1–5.
FPGA codesign
Custom PEs (systolic arrays) map models onto reconfigurable fabric. Anupreetham et al. reach 8× detection throughput; Sparse-YOLO targets YOLOv2 on CPU+FPGA.
Multimodal & AV
Li et al. weigh BEVDet (camera) vs. PointPillars (LiDAR) on FPGA/GPU. Hao & Chen survey codesign for multimodal multitask autonomous systems.

## Slide 9: Lightweight Models
Resource-constrained edge devices are limited in compute, memory, storage, energy and bandwidth. So, models must be small by design. Two approaches:
Human-designed
Expert-crafted efficient architectures
Depth-wise separable convolutions (MobileNets)
Group convolutions (Xception)
Proven, but time-consuming to design
Neural Architecture search
Let AI find the best architecture
Automated search: NASNet, AmoebaNet
Competitive — sometimes superior — accuracy
Limited by heavy hardware requirements

## Slide 10: Lightweight Models
Mobilenets
Left: Standard convolutional layer with batchnorm and ReLU. Right: Depthwise Separable convolutions with Depthwise and Pointwise layers followed by batchnorm and ReLU.
Problem: compared to normal convolution, depthwise convolution has a much lower capacity
Solution: Increase the depthwise convolution’s input and output channels to improve its capacity
      convolution’s cost only grows linearly, so the cost is still affordable.
However, this design is not memory-efficient for both inference and training.
Sandler, M., Howard, A., Zhu, M., Zhmoginov, A., & Chen, L. C. (2018). Mobilenetv2: Inverted residuals and linear bottlenecks. In Proceedings of the IEEE conference on computer vision and pattern recognition (pp. 4510-4520).

## Slide 11: Lightweight Models
SqueezeNet
(a) SqueezeNet
(b) SqueezeNet with simple bypass
(c) SqueezeNet with complex bypass
SqueezeNet
AlexNet-level accuracy with 50× fewer parameters (510× smaller).
Iandola, Forrest N., et al. "SqueezeNet: AlexNet-level accuracy with 50x fewer parameters and< 0.5 MB model size." arXiv preprint arXiv:1602.07360 (2016).

## Slide 12: Lightweight Models
MobileViT
MobileViT
MobileViT
Combines CNNs with Transformers to capture both local features and global context efficiently on mobile devices.
Mehta, Sachin, and Mohammad Rastegari. "Mobilevit: light-weight, general-purpose, and mobile-friendly vision transformer." arXiv preprint arXiv:2110.02178 (2021).
MobileViTV2
Improves MobileViT with separable self-attention, reducing computational cost and improving efficiency while maintaining strong accuracy.

## Slide 13: Lightweight Models
Additional studies
Xception / Flattened
Depth-wise separable & 1-D filters for fast, compact feedforward nets.
Bonsai / ProtoNN
Microsoft — tree & KNN models that fit tiny IoT devices (2 KB RAM Arduino).
EMI-RNN / FastGRNN
Kilobyte-sized RNNs — 72× less compute than LSTM, +1% accuracy.

## Slide 14: Acceleration Techniques
Overparameterization
Training needs many parameters to capture model fluctuations — but inference needs far fewer. So the model can be simplified after training, before edge deployment.
Less computation → lower power & time
Smaller footprint → lower-end devices
Complementary to hardware acceleration
ViT acceleration on FPGA
Auto-ViT-Acc
Mixed precision across transformer blocks; 0.47–1.36% higher Top-1 at the same bit-width.
ViA
Half-layer mapping + reuse engines beat NVIDIA Tesla V100 on energy efficiency.

## Slide 15: Acceleration Techniques : ViT acceleration on FPGA
Auto-ViT-Acc
Overview of Auto-ViT-Acc framework
Uses mixed-scheme quantization combining fixed-point + Power-of-Two (PoT) quantization.
Achieves 56.8 FPS vs. 10 FPS (~5.6× higher) than the FP32 FPGA baseline for DeiT-Base, with only 0.71% accuracy drop on ImageNet.
Li, Zhengang, et al. "Auto-vit-acc: An fpga-aware automatic acceleration framework for vision transformer with mixed-scheme quantization." 2022 32nd International Conference on Field-Programmable Logic and Applications (FPL). IEEE, 2022.

## Slide 16: Acceleration Techniques : ViT acceleration on FPGA
ViA
Overview of Auto-ViT-Acc framework
ViT-specific FPGA accelerator designed around the actual computation flow of Vision Transformers.
Reports about 5.2× higher energy efficiency than NVIDIA Tesla V100 and 4–10× improvement over prior FPGA accelerators.
T. Wang et al., "ViA: A Novel Vision-Transformer Accelerator Based on FPGA," in IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems, vol. 41, no. 11, pp. 4088-4099, Nov. 2022, doi: 10.1109/TCAD.2022.3197489

## Slide 17: Training & Inference on Edge
Where and How Models Learn
Architecture
Centralized
Client edges request services from a central server / cloud (client–server).
Decentralized
Peer-to-peer — edges share and consume resources directly, no central server.
Optimization goals
Processing efficiency — transfer learning, cache features, learn from peers
Communication efficiency — fewer, smaller updates; gradient quantization & sparsification
Why train at the edge?
Privacy Data stays local instead of going to a central server.
Personalization Models adapt to the data each device actually sees.
Robustness Less dependence on the network; resilient services.

## Slide 18: Training & Inference on Edge: Collaborative Training
Clone: learning on the edges
The idea. Each edge node trains on its own private data, then sends parameters to a central Parameter EdgeServer that aggregates and returns them.
Local data stays put
Nodes train on private datasets D₁…Dₙ — raw data never leaves the device.
Push / pull parameters
Only model parameters travel to and from the EdgeServer.
Lower latency & privacy
Demonstrated on connected vehicles — faster and more private than cloud training.
Clone framework
Sidi Lu, Yongtao Yao, and Weisong Shi. “CLONE: Collaborative learning on the edges”. In: IEEE Internet of Things Journal 8. 13 (2020), pp. 10222–10236.

## Slide 19: Training & Inference on Edge: Inference on Edge
Running Models Under Tight Budgets
Sumaiya et al. “Enhancing real-time inference performance for time-critical software-defined vehicles”. In: 2024 IEEE International Conference on Mobility, Operations, Services and Technologies (MOST). IEEE. 2024, pp. 101–113.
Optimization tool: TensorRT.
Converts PyTorch / TF / ONNX models and runs them in FP32, FP16 or INT8 precision modes to accelerate inference on edge devices.
Bridging task needs and device limits
Model design Lightweight nets (human-designed or searched) that fit edge hardware.
Model compression Prune, quantize, distill, low-rank — reuse of Lecture 5 techniques.
Optimization tools TensorRT precision modes trade accuracy for throughput & latency.
TensorRT-enabled framework for a Software-Defined Vehicle

## Slide 20: Training & Inference on Edge: Collaborative Inference
Many Cameras, One Tracker
Sidi Lu, Yongtao Yao, and Weisong Shi. “CLONE: Collaborative learning on the edges”. In: IEEE Internet of Things Journal 8. 13 (2020), pp. 10222–10236.
Figure 4.19 — Collaborative inference pipeline for multitarget multicamera tracking (Lu et al.).
Capture
Multiple camera video streams
Detect
YOLOv3 finds & boxes targets
Describe
Appearance (AD) + motion (MD) descriptors
Associate
Cosine + Mahalanobis distance match IDs
Collaborative inference pipeline for multitarget multicamera tracking

## Slide 21: Summary
Low-rank factorization reduces redundant weights and computation with minimal accuracy loss.
Model–hardware codesign balances performance requirements with available hardware resources.
Lightweight model design creates compact architectures suitable for edge deployment.
Edge training and inference keep data local while enabling efficient and fast execution.

## Slide 22: Practice
1
How does integrating hardware accelerators impact the design of machine learning models for edge deployment?
2
Discuss the role of software-hardware codesign in optimizing resource-constrained edge computing environments.

## Slide 23: References
Emily L Denton et al. "Exploiting linear structure within convolutional networks for efficient evaluation". In: Advances in Neural Information Processing Systems 27 (2014).
Misha Denil et al. "Predicting parameters in deep learning". In: Advances in Neural Information Processing Systems 26 (2013).
Tara N Sainath et al. "Low-rank matrix factorization for deep neural network training with high-dimensional output targets". In: 2013 IEEE International Conference on Acoustics, Speech and Signal Processing. IEEE. 2013, pp. 6655–6659.
Shikhar Tuli et al. “CODEBench: A neural architecture and hardware accelerator co-design framework”. In: ACM Transactions on Embedded Computing Systems 22. 3 (2023), pp. 1–30.
Minxuan Zhou et al. “TransPIM: A memory-based acceleration via software-hardware codesign for transformer”. In: 2022 IEEE International Symposium on High-PerformanceComputer Architecture (HPCA). IEEE. 2022, pp. 1071–1085.
Cong Hao and Deming Chen. “Software/hardware co-design for multi-modal multi-task learning in autonomous systems”. In: 2021 IEEE 3rd International Conference on Artificial Intelligence Circuits and Systems (AICAS). IEEE. 2021, pp. 1–5.
Sandler, M., Howard, A., Zhu, M., Zhmoginov, A., & Chen, L. C. (2018). Mobilenetv2: Inverted residuals and linear bottlenecks. In Proceedings of the IEEE conference on computer vision and pattern recognition (pp. 4510-4520).
Mehta, Sachin, and Mohammad Rastegari. "Mobilevit: light-weight, general-purpose, and mobile-friendly vision transformer." arXiv preprint arXiv:2110.02178 (2021).
Li, Zhengang, et al. "Auto-vit-acc: An fpga-aware automatic acceleration framework for vision transformer with mixed-scheme quantization." 2022 32nd International Conference on Field-Programmable Logic and Applications (FPL). IEEE, 2022.
T. Wang et al., "ViA: A Novel Vision-Transformer Accelerator Based on FPGA," in IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems, vol. 41, no. 11, pp. 4088-4099, Nov. 2022, doi: 10.1109/TCAD.2022.3197489.
Sidi Lu, Yongtao Yao, and Weisong Shi. “CLONE: Collaborative learning on the edges”. In: IEEE Internet of Things Journal 8. 13 (2020), pp. 10222–10236.
Sumaiya et al. “Enhancing real-time inference performance for time-critical software-defined vehicles”. In: 2024 IEEE International Conference on Mobility, Operations, Services and Technologies (MOST). IEEE. 2024, pp. 101–113.